## Slide 1
Controls &
Instrumentation:
Control Rod Simulator (Dye Control Regulator)
Group 9: Siddharth, Zhiyu, Cecilia, Issa, Kira
Nuclear Innovation Challenge

## Slide 2
Challenge Problem :
For controller to regulate the same outputs within the limits of the existing physical constraints
Dye Concentration Regulator
Physical System
(Reactor stability control)
Studying the flow, sensor accuracy, and system response
State estimation and safety supervision
Comparing controllers over multiple tests, watching for “unsafe” conditions

## Slide 3
Relevance and Background
  SMRs use boron in their control rods
    Controlling rate of reaction
  Helped in past nuclear disasters
  Too much boron, reactor shuts off
  Too little boron, no coolant
  Emergency shutdown (scram)
(Zoomie & Zoomie, 2024)
Relevance
Impact

## Slide 4
Used to pump solution from the reactor so that the reactor doesn’t exceed 450mL.
Control Rod Simulator
01
02
03
  Green Dye simulates boron in control rods
  Managing rate of reaction
  Highly concentrated
Reactor
Clear
Solution
Dyed
solution
  No dye here is added.
  Feeds to reactor to dilute concentration when it’s too high
  Starts as a clear solution
  Dyed solution slowly feeded in until ideal concentration
  Scram if no dye for too long
Waste Beaker
04

## Slide 5
Experiment and Observations
  Find absorbtion using Beer-Lambert’s law and measured frequency from light sensor
  Find concentration using:
c = (number of drops * 0.05ml) / 350ml
  Measured flow rates for calibration
  Created an app connected to the arduino, having separate buttons to control each flow
Pump Calibrations (Flow Rates) - false
Waste: 9.4mL/s
Clear: 7.95mL/s
Dye: 8.9mL/s
Concentration Calibrations
  Got frequency from sensors
  Calculate absorbance from frequency, verify concentration
Graph showing A, absorbance, depending on c, concentration of mL of dye per mL of water)
  Minimized external light
  Use camera sensors to measure water levels, to control the volume
  Testing the controller

## Slide 6
Setbacks
Concentration Calibration
External Light
  On second day, outside light became darker
  Moved to a brighter area
  Used cardboard box with incision for flashlight to minimize other light
  Wrong calibration and anomalous values because of the use of two identical solutions
  False usage of units
  Unnessary flow calibrations

## Slide 7
Safety and Regulations
  Ability to slow or halt fission
  Disaster recognition
Managing concentration:
  Minimizing nuclear disasters
  Control rod lowering is automated - solution would not require further worker attention
Stakeholder impact:
  Nuclear safety control act 2.1.10: neutron detector requirement
  Nuclear safety control act 2.2.5: neutron measurement system
(Government of Canada, Public Works and Government Services Canada, Public Services and Procurement Canada, Integrated Services Branch, Canada Gazette, 2025)
Regulation alignment:
Notes: https://gazette.gc.ca/rp-pr/p2/2025/2025-10-08/html/sor-dors196-eng.html
A.2.1.10 Neutron detectors
Especially designed or prepared neutron detectors for determining neutron flux levels within the core of a nuclear reactor within the meaning of paragraph A.2.1.1.
A.2.2.5 Neutron measurement systems for process control
Neutron measurement systems especially designed or prepared for integration and use with automated process control systems in reprocessing plants referred to in paragraph A.2.2.

## Slide 8
Citations
Government of Canada, Public Works and Government Services Canada, Public Services
and Procurement Canada, Integrated Services Branch, Canada Gazette. (2025, October 9).
Canada Gazette, Part 2, Volume 159, Number 21: Regulations amending certain regulations made under the Nuclear Safety and Control Act (Imports, Exports and Safeguards). https://gazette.gc.ca/rp-pr/p2/2025/2025-10-08/html/sor-dors196-eng.html
Borates in nuclear energy: Preventive and emergency nuclear safety. (n.d.). https://www.borax.com/applications/nuclear-energy
Zoomie, & Zoomie. (2024, May 5). Control rods in nuclear reactors – it’s all about neutrons. Nevada Technical Associates, Inc. |. https://www.ntanet.net/control-rods-in-nuclear-reactors-its-all-about-neutrons/

## Slide 9
AI Disclosure
AID Statement: Artificial Intelligence Tool: Claude (app, pro version); Conceptualization: Used to simplify some technical concepts mentioned in GitHub and explain in the simple way the functionality of the control rods in SMR; Execution: Modified and debugged the code used to run the Arduino to simulate the physical system of the dye concentration regulator; Visualization: Generated an app/dashboard Pump Control that gives commands to Arduino and is used to regulate the running pump tests, while adapting to the base dye concentration control. Generated the graph of concentration levels.

## Slide 10
Thank You